## Slide 1: Appendix

## Slide 2
Appendix I.
The scope of the method development in this research is limited to modeling NPP software failures for ‘failure on-demand’ scenario (focus of NPP PRA model).
The method assumes FBD programs exactly represent the initial software requirements; thus, test cases generated from FBD program reflect all the on-demand situations of that NPP safety software.
* FBD : function block diagram / PRA : probabilistic risk assessment / CTL : Computation tree logic / LTL : Linear temporal logic / VIS : Verification Interacting with Synthesis / SMV : Symbolic model verifier / SDS : software design specifications (e.g. design documents, FBD files)
Software life cycle and related development/verification processes of a typical NPP safety software
Development Process
V&V process
Software Life Cycle
1) Requirement
2) Design
3) Implementation
4) Test ing
5) Installation/Checkout
Natural-language specification
FBD programs
FBD programs
FBD programs
Executable machine code for PLC
Automatic synthesis
Compiled into
NuSCR toFBD
Formal verification
CTL model checking
(Cadence SMV)
NuSRS
Equivalence
Checking (VIS)
FBD design verification
FBDVerifier
LTL model checking
(Cadence SMV)
* Existing tools used for conducting the task.
The test cases are derived from SDS
Executable code is used for testing
Notes:   https://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=4814957

## Slide 3
Appendix II.
Basic operation of NPP Safety-graded PLC
  1) Fetch: the executable code in the memory map is fetched.
  2) Decode: the fetched code is decoded into a specific instruction set.
  3) Read: the address is generated and the operands are read from the registers.
  4) Execute: the operation of the decoded instruction set is performed and the operation results are stored in the CPU register or the memory.
reads inputs
Computation &
Logic Execution
updates variable
Internal Variable
Safety-critical PLC
Generate output
Output signal to relay/controller
HW
Inputs from plant operation
Operator action
SW
Plant Process Parameter
Inputs from other digital system
I/O Memory area
PLC Memory
DO/SDL/SDN
AI/DI/SDL/SDN
I/O Memory area
Test Module
Operating mechanism of a Typical NPP safety PLC
Block diagram of a typical PLC CPU architecture
Notes:   Especially, the programmable logic controller, or PLC, has been used for safety systems which is critical to the safe shutdown of NPP in case of accident.
  However, unlike hardware-based analog I&C system, the use of hardware-software-combined digital I&C system in NPP has raised issues in terms of PRA,
  Since it was very hard to capture the software failure
  The software reliability growth model have been used in commercial software engineering field;
  however, the lack of software failure data due to short operation history made SRGM not applicable to reliability quantification.
  BBN is a kind of model-based method that aggregates various SW development information and generates a model;
  however, since the parameter quantification and model generation is often based on experts’ opinion; so we expect high uncertainty in the result of BBN model.
  Another method is to quantify SW reliability based on test result.
  Especially, black-box test-based method is a method which takes samples from SW operational profile and quantify the reliability using the statistical analysis based on test results;
  however, the method inherently suffers from addressing the test coverage and often has long test execution time.

## Slide 4
Appendix III.
Development of NPP safety software test-bed (NSTM)
  1) Emulation of microprocessor architecture of POSAFE-Q PLC
    CPU registers (30 registers)
      Extended-precision registers – extended-precision floating-point expression
      Auxiliary registers – indirect addressing, 32-bit integer/logical expression
      Other registers : system functions (e.g., stack, condition, block repeat)
    Memory map (16 Mbyte; 0x000000 ~ 0xFFFFFF)
      16Mbyte 32-bit words of program, data, I/O space
      Accessible by various addressing modes (e.g. direct, indirect, immediate)
TMS320C3x CPU registers and Memory map
CPU and memory emulation in test-bed (C code)
CPU registers
Memory map (RAM, ROM)
Create virtual CPU register and Memory map
Notes:   a software test-bed is developed that captures both the internal (CPU and memory architecture) and external (states of program input and output variables) aspects of the PLC scan cycle. The test-bed is developed in C code by emulating the PLC microprocessor architecture, such as the CPU register and the memory map [24] and the assembly language instructions.

## Slide 5
Appendix III.
Development of NPP safety software test-bed (NSTM)
  2) Implementation of microprocessor (TMS320c3x) instruction sets
    Total of 118 assembly language instructions
    Types of instruction set:
      1) Load and store
      2) 2-operand arithmetic/logical
      3) 3-operand arithmetic/logical
      4) Program control
      5) Interlocked operations
      6) Parallel operations
Description of LDI (load integer) instruction set operation
Emulated operation of LDI (load integer) instruction set in test-bed
Decode machine code
Notes:   a software test-bed is developed that captures both the internal (CPU and memory architecture) and external (states of program input and output variables) aspects of the PLC scan cycle. The test-bed is developed in C code by emulating the PLC microprocessor architecture, such as the CPU register and the memory map [24] and the assembly language instructions.

## Slide 6
V&V of NPP safety software test-bed (NSTM)
  Instruction set testing (using CppUnit*) : A total of 2090 unit test cases were developed and tested to verify the correctness of emulated instruction set.
Appendix IV.
Start
Develop unit test cases for instruction set
Implement unit test cases to test-bed
Verify the instruction output with expected output
End
Debug/ Review
Yes
No
Example of unit test case developed for LDI (load integer) instruction
Contains unit test cases for OR instruction set
Result of unit testing for each instruction set
Summary of test result for all unit test cases
Result of unit testing for software test-bed
Verification process of the software test-bed with instruction set unit test cases
* CppUnit : xUnit tool for C/C++ programming languages
Notes:   D:\Cppexample\Cppunit_for_C_4

## Slide 7
V&V of NPP safety software test-bed (NSTM)
  Functional testing : The test cases for benchmark programs were developed and tested to verify the overall functionality of test-bed.
    Lamp On/Off software : 22 cases for Lamp On scenario
    KNICS IDiPS-RPS BP software : 659 cases for trip scenario (15 trip logics)
Appendix IV.
Test case file
Expected output file
Program file (executable code)
Test result file
Screenshot of test-bed execution
Notes:   D:\Cppexample\Cppunit_for_C_4

## Slide 8
Appendix V.
Theoretical Basis of Exhaustive Test Case Generation
  Example algorithms to solve an SAT example (SSC):
,
: Satisfiable
: Unsatisfiable
, , ,
SCC
SCC
SCC
SCC
Check satisfiability:
If and are at same SCC, unsat
else, sat
→ in case, sat
Derive interpretation:
For each SCC , set vertices’ value to false,
(to avoid true → false cases), and check the contradictions between SCCs.
→ in case,
* SCC : Strongly Connected Component (A directed graph is strongly connected if there is a path between all pairs of vertices)
Notes:   https://people.eecs.berkeley.edu/~sseshia/pubdir/SMT-BookChapter.pdf
  https://algospot.com/wiki/read/2-SAT
  http://blog.naver.com/PostView.nhn?blogId=kks227&logNo=220803009418
  Other algorithms: Floyd-warshall, DPLL

## Slide 9
Appendix V.
Theoretical Basis of Exhaustive Test Case Generation
  Expansion from SAT to SMT problem:
* read(a, i) means to read the i-th element in array a.
arithmetic
Arrays
Uninterpreted functions
Abstract to Propositional Logic
Find satisfying assignment
Determine if consistent according to theory solver (arithmetic, equalities, etc.)
Notes:   https://people.eecs.berkeley.edu/~sseshia/pubdir/SMT-BookChapter.pdf
  http://fmv.jku.at/rerise14/rerise14-smt-slides-1.pdf
  Dpll
  https://ptolemy.berkeley.edu/projects/embedded/eecsx44/fall2011/lectures/SATSolving.pdf
  https://en.wikipedia.org/wiki/DPLL_algorithm

## Slide 10
Appendix VI.
NPP safety software language – FBD/LD program
  FBD is a graphical language used for PLC design that describes the function between input and output variables expressed with a set of elementary blocks.
    Definition of Function Block (FB)
    Definition of Component FBD (Comp_FBD)
    Definition of System FBD (Sys_FBD)
FB = <Name, IP, OP, BD>
  Name : a name of function block,
  IP: a set of input ports,
  OP: a set of output ports,
  BD: behavioral description of function block.
Component_FBD = <FBs, T, I, O>,
  FBs : a set of FBs,
  T: A set of transition () btw FBs
  ∀() ∈ T
  I: a set of FB.IP not included in T,
  O: a set of FB.OP not included in T,
System_FBD = <FBDs, T, I, O>,
  FBDs : a set of Component_FBDs,
  T: a set of transition (FBDi.Om,FBDj.In) btw Component_FBDs, ∀() ∈ T
  I: a set of FBD.I not included in T,
  O: a set of FBD.O not included in T,

## Slide 11
Translation from FBD into SMT format
  The FBD-to-SMT translation rules are developed based on FBD formal definition.
  The translation starts with generating SMT formulas for all FBs, and continues for component FBD and system FBD.
Appendix VII.
Function Block (FB = <Name, IP, OP, BD>)
Component FBDs
(Comp_FBD = <FBs, Tcomp, I, O>)
System FBDs
(Sys_FBD = <Comp_FBDs, Tsys, I, O>)
Name = ADD2_DINT
IP = {EN, IN1, IN2}
OP = {ENO, OUT}
BD = IN1 + IN2
def ADD2_DINT(EN, IN1, IN2):
# -- define BD of FB --
BD = IN1 + IN2
# -- define ENO/outputs of FB --
ENO1 = If(EN, True, False)
OUT1 = If(EN, BD, OUT)
# -- return ENO/outputs of FB --
return ENO1, OUT1
FBs = {LE_REAL, MOVE_BOOL, …}
= {MOVE_BOOL.in_EN = LE_REAL.OUT(TRIP_LOGIC), …}
I = {EN, PV_OUT, TSP, HYS}
O = {ENO, TRIP_LOGIC, TSP}
def RESET_FALLING(EN,PV_OUT,in_HYS, in_PV_OUT,…,ENO,…,out_TRIP_LOGIC) # -- temporary variables --
temp1 = False
# -- function operation --
LE_REAL0_OUT = LE_REAL(True, in_PV_OUT , in_TSP, …) temp1 = And(LE_REAL0_OUT, Not(in_TRIP_LOGIC)) TRIP_LOGIC1 = MOVE_BOOL(temp1, True, …) # return ENO/outputs of FB --
ENO1 = If(EN, True, False)
TRIP_LOGIC5 = If(EN, TRIP_LOGIC4 , out_TRIP_LOGIC) return ENO1, …, TRIP_LOGIC5
#define FB
def BP_k_Trip_LogicA(BP_k_Trip_LogicA_in):
# define ENO and outputs of FB
…, _6_TRIP_LOGIC2, … = RESET_FALLING( …, _6_TRIP_LOGIC1, …)
…, TRIP_DECISION51_out_TRIP, … = TRIP_DECISION(…, _6_TRIP_LOGIC2, …) …
# return ENO and outputs of FB
return BP_k_Trip_LogicA_out
Comp_FBDs = {_6_RESET_FALLING, _6_TRIP_DECISION, …}
= {_6_TRIP_DECISION.in_TRIP_LOGIC = _6_RESET_FALLING.out_TRIP_LOGIC, …}
I = {_6_HYS, _6_TRIP_LOGIC, …}
O = {_6_TRIP, _6_TSP, …}
Transitions btw FBs
Transitions btw Comp_FBDs
Notes:   ----------------------------

## Slide 12
Appendix VII.
Translation of Function Block (FB) to SMT formula
  Rule 1 : Define the elements of FB (name, I/O ports)
  Rule 2 : Define the FB operation
  Rule 3 : Define the FB output ports
  Rule 4 : Return the FB output ports
#define FB
def ADD4_DINT(EN, IN1, IN2, IN3, IN4, ENO, OUT):
# define BD of FB
BD = IN1 + IN2 + IN3 + IN4
# define ENO and outputs of FB
ENO2 = If(EN, True, False)
OUT2 = If(EN, BD, OUT)
# return ENO and outputs of FB
return ENO2, OUT2
FBD-to-SMT translation rules for FBs
Formal definition and translation for example FB, ADD4_DINT

## Slide 13
01 02 03 04 05 06 07 08 09 10 11 12 13 14 15 16 17 18 | # Define Component FBD def RESET_FALLING__(EN, HYS, PV_OUT, ENO, TRIP_LOGIC, TSP): … # Define Component FBD operation and all translation relation ENO__1__RESET_FALLING, OUT__1__RESET_FALLING = LE_REAL(True, PV_OUT, TSP, ENO__1__RESET_FALLING, OUT__1__RESET_FALLING) __tbool = If(True, And(OUT__1__RESET_FALLING,Not(TRIP_LOGIC)), __tbool) … ENO__3__RESET_FALLING, OUT__3__RESET_FALLING = MOVE_BOOL( __tbool, True, ENO__3__RESET_FALLING, OUT__3__RESET_FALLING) … # Define ENO and output of Component FBD ENO2 = If(EN, ENO1, False) TRIP_LOGIC2 = If(EN, TRIP_LOGIC1, TRIP_LOGIC) TSP2 = If(EN, TSP1, TSP) # return ENO and outputs of Component FBD return ENO2, TSP2, TRIP_LOGIC2
Appendix VII.
Translation of Component FBD (Comp_FBD) to SMT formula
  Rule 5 : Define the elements of component FBD (name, I/O ports)
  Rule 6 : Define the program flow according to execution order of FBs in Comp_FBD
  Rule 7 : Define the Comp_FBD output ports
  Rule 8 : Return the Comp_FBD output ports
FBD-to-SMT translation rules for component FBDs
An example of translation for the component FBDs
Temporary variables are used to model a set of transitions btw FBs.

## Slide 14
Appendix VII.
Translation of System FBD (Sys_FBD) to SMT formula
  Rule 9 : Define the elements of system FBD (name, I/O ports)
  Rule 10 : Define the program flow according to execution order in Sys_FBD
  Rule 11 : Define the Sys_FBD output ports
  Rule 12 : Return the Sys_FBD output ports
FBD-to-SMT translation rules for system FBD
An example of translation for the system FBD
(1)
(2)
01 02 03 04 05 06 07 08 09 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 | # Define System FBD def BP___k_Trip_LogicA(BP____k_Trip_LogicA_in): … # rung 147 RESET_FALLING50_out_ENO, … RESET_FALLING50_out_TRIP_LOGIC = RESET_FALLING(RESET_FALLING50_in_EN, RESET_FALLING50_in_HYS, … , RESET_FALLING50_out_ENO, …, RESET_FALLING50_out_TRIP_LOGIC) _6_TRIP_LOGIC__2 = If(RESET_FALLING50_out_ENO, RESET_FALLING50_out _TRIP_LOGIC, _6_TRIP_LOGIC__1) … # rung 148 TRIP_DECISION51_in_TRIP_LOGIC = _6_TRIP_LOGIC__2 … TRIP_DECISION51_out_ENO, …, TRIP_DECISION51_out_TRIP, TRIP_DECISION51_out_PTRIP = TRIP_DECISION(TRIP_DECISION51_in_EN , TRIP_DECISION51_in_TRIP_LOGIC, …, TRIP_DECISION51_out_TRIP) _6_TRIP__2 = And(TRIP_DECISION51_out_TRIP,Not(_6_OB_START_STA__1)) … # Define outputs of Sys_FBD BP____k_Trip_LogicA_out = [] BP____k_Trip_LogicA_out.append(_6_TRIP__2) … # Return outputs of Sys_FBD return BP____k_Trip_LogicA_out

## Slide 15
Background on SMT Solving Techniques – DPLL algorithm
  DPLL algorithm is a complete, backtracking-based search algorithm for solving the CNF-SAT problem.
    Complete: guarantees to find a solution if there is any
    Backtracking: exercise all possible paths to solve SAT/SMT problem.
  Existing SMT solver: CVC4 (Stanford), Yices (SRI), Z3 (Microsoft) [7]
    Z3 ~ DPLL-(T), a theorem prover for first-order logic about an arbitrary theory T.
Appendix VIII.
p
q
r
1
1
1
0
0
0
1
0
1
{ }
* DPLL: Davis–Putnam–Logemann–Loveland
invalid
invalid
invalid
invalid
valid
Notes:   In order to finally generate test cases, we need to solve the translated SMT formula.
  There are several existing SMT solving techniques which can be applied in this research.
  DPLL algorithm is one of the representative SMT solving techniques, which is a search-based algorithm,
  1) that is complete, meaning 1) it guarantees to find a solution if there is any,
  2) and is based on backtracking meaning 1) it enables finding all solution to a specific problem.
  For example, for the formula in conjugate normal form,
  The algorithm incrementally builds candidates to the solutions,
  and abandons a candidate, or backtracks, as soon as it determines that the candidate cannot possibly be completed to a valid solution.
  And it repeats this process until it finds a valid model that makes the formula valid.
  There are several powerful tools that solve the complex formulas with hundreds of variables.
  Among those tools, in this research, we will utilize the Z3 SMT solver leveraging its ability for its advanced model generation capability,
  along with supporting APIs for other programming languages (e.g. Python/C/Java).
  ----------------------
  https://en.wikipedia.org/wiki/Clause_(logic)#Empty_clauses
  https://www.youtube.com/watch?v=i8SDkVGclYk
  Completeness: https://en.wikipedia.org/wiki/Completeness
  Backtracking: https://cs.uwaterloo.ca/~vanbeek/Publications/survey06.pdf
  https://en.wikipedia.org/wiki/Backtracking
  Basic SAT algorithm:
  https://www.win.tue.nl/~jschmalt/teaching/2IMF20/BMC-lecture_slides_SAT.pdf
  PPT 대사에 위 link의 introduction에 있는 내용을 말하자 (간단하게만)

## Slide 16
SMT Solving Technique – DPLL algorithm ()
  UP(, ); - Unit-propagate
  if contains the empty clause () then return;
  if is empty formula (), then exit with model of U;
  a literal containing an atom from ;
  ;
  ;
Appendix VIII.
An example of SMT solving using DPLL algorithm
└
└
└
└ return model
Notes:   https://en.wikipedia.org/wiki/Clause_(logic)#Empty_clauses
  https://www.youtube.com/watch?v=i8SDkVGclYk
  Before mentioning about the exhaustive test case generation, I would like to discuss some important aspects in proposed test case generation procedure for a single test case.
  The developed algorithm for a single test case for safety software includes three parts:
  1) first, analyzing translating the program under test and defining the SW program as a formula to be solved.
  2) second, defining test requirements (or the target software output);
  3) third, solving the test requirements by checking the satisfiability and finding a model (or solution for the software inputs).
  In result, if the SW program is satisfiable for the software output the tester defined,
  the algorithm would retrieve one solution which satisfies the formula and this will be saved as a single test case.

## Slide 17
Appendix VIII.
Z3: DPLL-based SAT + Theory solver (Arithmatic, Array, Bit-vector)
  Invoke DPLL(T) for theory T = LIA (Linear Integer Arithmetic)
    Map : {, , , }
    Invoke SAT solver:
      Propagate: , Propagate:
      Decide:
    Invoke theory solver for LIA on: {, , }
      is LIA-unsatisfiable.
      is added to list of clauses.
Notes:   DPLL algorithm to incorporate reasoning about a theory T
  https://people.eecs.berkeley.edu/~sseshia/pubdir/SMT-BookChapter.pdf
  http://fmv.jku.at/rerise14/rerise14-smt-slides-1.pdf
  Dpll
  https://ptolemy.berkeley.edu/projects/embedded/eecsx44/fall2011/lectures/SATSolving.pdf
  https://en.wikipedia.org/wiki/DPLL_algorithm
  http://homepage.divms.uiowa.edu/~ajreynol/pres-dpllt15.pdf
  https://web.stanford.edu/class/cs357/lectures/lec9.pdf
  https://www.cs.tau.ac.il/~msagiv/courses/ATP/smt.pdf

## Slide 18
Appendix VIII.
Z3: DPLL-based SAT + Theory solver (Arithmatic, Array, Bit-vector)
  Invoke DPLL(T) for theory T = LIA (Linear Integer Arithmetic)
    Invoke SAT solver:
      Backtrack decision on C ()
      Propagate
      Propagate
    Invoke LIA on: {, , , }
      is LIA-unsatisfiable.
      is added to list of clauses.
    No decisions to backtrack The formula is LIA-unsatisfiable.
Notes:   DPLL algorithm to incorporate reasoning about a theory T
  https://people.eecs.berkeley.edu/~sseshia/pubdir/SMT-BookChapter.pdf
  http://fmv.jku.at/rerise14/rerise14-smt-slides-1.pdf
  Dpll
  https://ptolemy.berkeley.edu/projects/embedded/eecsx44/fall2011/lectures/SATSolving.pdf
  https://en.wikipedia.org/wiki/DPLL_algorithm
  http://homepage.divms.uiowa.edu/~ajreynol/pres-dpllt15.pdf
  https://web.stanford.edu/class/cs357/lectures/lec9.pdf

## Slide 19
Appendix IX.
Single Test Case Generation for NPP Safety Software
  Algorithm for a single test case generation of an example FBD program
1-1) Declaration of the FBD variables (line 6~20)
1-2) Declaration of FBD program logic (line 22~39)
2-1) Assertion of test requirement (line 41~42):
3-1) Check satisfiability given constaint (line 45):
Z3 input file for one test case generation of FBD program
STEP 1: Define problem set
STEP 2: Define test requirement
STEP 3: Solve test requirement
An example FBD program
3-2) Find a model for FBD program (line 46):
Notes:   This shows an single test case generation algorithm for an example FBD program.
  1) Environmental setting (lines 1~4): Commands pertinent to our application of SAT/SMT framework are defined here.
  2) Declaration of the FBD variables (line 6~20):
  All variables and constants included in the target FBD program are declared here.
  3) Declaration of FBD program logic (line 22~39):
  The FBD blocks used in the program as well as the program logic flow are declared here.
  4) Assertion of test requirement (line 41~42):
  The software output is defined as a test requirement and add it as a constraint of the model to be solved.
  5) Find a model for FBD program (line 44~46):
  check() finds whether the set of formulas is satisfiable.
  model() is used to retrieve an interpretation that makes all formulas true and return as a test case.

## Slide 20
Single Test Case Generation for NPP Safety Software
  Execution of a single test case generation algorithm for example FBD program
Appendix IX.
Definition of function blocks
Screenshot of single test case generation algorithm execution
Z3 input file for single test case generation of FBD program
An example FBD program
Notes:   Definition of function blocks (explicitly defined based on IEC 61131-3 std.)
  So this shows the execution result of a single test case generation algorithm.
  After it check the satisfiability, it return one model that satisfies the formula given the test requirement.

## Slide 21
Appendix X.
Exhaustive Test Case Generation for NPP Safety Software
  To derive all interpretations (solutions) to FBD program, at each iteration, the algorithm:
    1) Derives the model from satisfiability check
    2) Saves the model as a single test case
    3) Adds a new constraint that negates the last found interpretation to the test requirement at each iteration.
    4) If the formula is unsatisfiable, return the derived model as exhaustive test cases.
      Unsatisfiable means there exist no interpretation (solution) that evaluates a given formula to true under given constraints.
Exhaustive test case generation algorithm for FBD programs
1)
2)
3)
4)
Notes:   This shows the detailed aspects of exhaustive test case generation proposed in this study utilizing SAT/SMT framework.

## Slide 22
Appendix XI.
Example of Exhaustive Test Case Generation for Simple FBD Program
TestCase1 = [PV_OUT = 17780, TSP = 17780, TRIP_LOGIC = False]
1st Iteration result
TestCase2 = [PV_OUT = 17781, TSP = 17781, TRIP_LOGIC = False]
2nd Iteration result
The negation of TestCase1 is added to TR2 as new constraint
TestCase2 generated for TR2
Execution result of exhaustive test case generation algorithm for an example PLC program
Initial Test Requirement (TR1)
TestCase1 generated for TR1
Notes:   This shows an example illustration on how FBDET algorithm generates exhaustive test cases for a specific FBD program.
  At the first iteration, the solver checks that the formula is satisfiable, generated the model.
  Here the new constraint, is formulated as the negation of the solution found in current iteration,
  And is added as a new constraint to the original formula to be solved at next iteration,
  Therefore, the derived model at the second iteration is exclusive from the model derived from first iteration.
  This process is repeated until

## Slide 23
Appendix XI.
Example of Exhaustive Test Case Generation for Simple FBD Program
Execution result of exhaustive test case generation algorithm for an example PLC program
TestCase66 = [PV_OUT = 17784, TSP = 17789, TRIP_LOGIC = False]
66th and 67th Iteration result
Generated Exhaustive Test Cases (TestSet)
…
TestCase66 generated for TR66
Given TR67, the formula is unsatisfiable → return TestSet
Notes:   until the SMT solver return the satisfiability check result as unsatisfiable.
  As a result of the FBDET algorithm execution, the test case file are generated which lists the name of the variables and their states